## Slide 1: Amplitude Modulation
Gaurav S. Kasbekar
Dept. of Electrical Engineering
IIT Bombay

## Slide 2: Introduction
Information that needs to be transmitted over a communication channel usually a baseband signal
Recall: message signal shifted to a high-frequency band before transmission
“Carrier” is a sinusoid of high frequency
Modulation: process by which some characteristic of a carrier (e.g., amplitude, frequency, phase) varied in accordance with a modulating wave (message signal)
  result of modulation referred to as “modulated wave”
Modulation performed at transmitter
At receiver, message (baseband) signal recovered using “demodulation”
We now study “amplitude modulation” (AM), in which amplitude of a carrier varied in accordance with message signal
Later, we will study frequency modulation (FM) and phase modulation (PM)

## Slide 3: Amplitude Modulation (AM)
Consider a carrier wave:
  ,
  where is “carrier amplitude” and
  is “carrier frequency”
Note: for simplicity, in 1), the phase of the carrier assumed to be
Let be message signal, which is a baseband signal
AM: process in which amplitude of the carrier wave varied about a mean value, linearly with message signal
Amplitude modulated (AM) wave given by:
  where called “amplitude sensitivity”

## Slide 4: Example
Recall: AM wave given by:
Fig. shows and in the cases (i) for all , and (ii) for some
Ref: “Communication Systems” by S. Haykin and M. Moher, 5th ed

## Slide 5: Envelope Detection
Consider a signal
If varies slowly in comparison with the carrier , then:
  called the envelope of
Recall: AM wave given by:
Under some conditions, envelope of AM wave has same shape as message signal
So by detecting envelope at receiver of communication system, message signal can be recovered
We will later see that envelope detection is a simple and inexpensive operation
Hence, next we study sufficient conditions under which envelope detection can be used at receiver to recover message signal from AM wave

## Slide 6: Envelope Detection (contd.)
Recall: AM wave given by:
Envelope of has same shape as if following conditions satisfied:
for all
,
  where is message bandwidth (highest frequency component of message signal )
If 2) is not satisfied, then an envelope cannot be visualized (and therefore detected) satisfactorily
1) ensures that for all
  so is envelope, and can be easily recovered from envelope
If 1) is not satisfied then for some values of , can happen
  called “envelope distortion”; then, difficult to obtain from envelope
  carrier wave said to be “overmodulated”

## Slide 7: Spectrum of AM Wave
Recall: AM wave given by:
Fourier transform of
Fig. shows and
Ref: “Communication Systems” by S. Haykin and M. Moher, 5th ed

## Slide 8: Spectrum of AM Wave (contd.)
For positive frequencies, portion of spectrum of an AM wave:
  lying above referred to as “upper sideband”
  lying below referred to as “lower sideband”
For negative frequencies, portion of spectrum:
  lying below referred to as upper sideband
  lying above referred to as lower sideband
“Transmission bandwidth” of an AM wave (amount of bandwidth required to transmit it):
  twice of message bandwidth
Thus, AM is wasteful of bandwidth
Ref: “Communication Systems” by S. Haykin and M. Moher, 5th ed

## Slide 9: Example: Single-Tone Modulation
Suppose message signal is:
Corresponding AM wave:
  ,
  where
To avoid envelope distortion due to overmodulation, we need:
Fourier transform of :
  Fig. shows , carrier signal , modulated wave (when ) and their Fourier transforms
  Average power delivered to a ohm resistor by :
Simplifies to:
  the three terms in 1) correspond to carrier power, upper side-frequency power and lower side-frequency power respectively
Ref: “Communication Systems” by S. Haykin and M. Moher, 5th ed

## Slide 10: Example: Single-Tone Modulation (contd.)
Recall:
  AM wave: , where
  Average power:
  the three terms in 1) correspond to carrier power, upper side-frequency power and lower side-frequency power respectively
Ratio of total sideband power to total power in modulated wave:
  increases in ; maximum value at
Since useful information (message signal ) is conveyed only by sidebands:
  at most, only of the total transmitted power spent in conveying useful information
  rest used in sending carrier signal, which is independent of
This example shows that AM is wasteful of transmitted power
However, later we will see that due to transmission of carrier signal, it is simple and inexpensive to demodulate AM signal at receiver
  if carrier signal is not transmitted, then receiver complexity increases
For what kind of communication is AM well-suited?
  for broadcast transmission, in which there are a huge number of receivers for every transmitter
  economical to have one expensive high-power transmitter and many simple, inexpensive receivers
Hence, AM broadcasting systems are popular
However, for point-to-point links (one receiver per transmitter), wasteful to spend large amount of power in sending carrier signal
  we will study other techniques that overcome this shortcoming of AM

## Slide 11: Summary: Advantages and Disadvantages of AM; Alternatives
Advantages of AM:
  Modulation and demodulation process simple
  Inexpensive receivers can be used
Limitations of AM:
  Wasteful of bandwidth since transmission bandwidth is twice of message bandwidth
    Amplitude and phase spectra of upper and lower sidebands are symmetrical about carrier frequency
    Sufficient to transmit only one sideband to convey all information contained in message signal; but AM transmits both sidebands
  Wasteful of transmitter power since large amount of power spent in transmitting carrier signal, which is independent of message signal
Next, we will study some alternative modulation/ demodulation techniques:
  more efficient in terms of transmission bandwidth and/ or transmitter power
  but modulation and/ or demodulation process more complex
Alternative modulation/ demodulation techniques:
  Double Sideband-Suppressed Carrier (DSB-SC) Modulation
  Vestigial Sideband (VSB) Modulation
  Single Sideband (SSB) Modulation

## Slide 12: Double Sideband-Suppressed Carrier (DSB-SC) Modulation
Let (respectively, ) be message signal (respectively, carrier signal)
In DSB-SC, modulated wave is product of and :
undergoes a phase reversal whenever crosses zero (see fig.)
So envelope of a DSB-SC signal different from message signal
  Envelope detection cannot be used for demodulation
Ref: “Communication Systems” by S. Haykin and M. Moher, 5th ed

## Slide 13: DSB-SC Modulation (contd.)
Recall: DSB-SC modulated wave:
Fourier transform of
Fig. shows spectra of and
How can DSB-SC signal be demodulated at receiver?
  by multiplying it by and low-pass filtering
As in AM, transmission bandwidth is twice of message bandwidth
But carrier signal suppressed, which saves transmission power
Ref: “Communication Systems” by S. Haykin and M. Moher, 5th ed

## Slide 14: Quadrature-Carrier Multiplexing
Recall: in DSB-SC and in AM, transmission bandwidth is twice of message bandwidth
  wastage of bandwidth
Quadrature-carrier multiplexing or quadrature-amplitude modulation (QAM):
  a more bandwidth-efficient scheme
Let and be two independent message signals
  each is a baseband signal with bandwidth
Under QAM, modulated signal given by:
has non-zero frequency content in the band:
So bandwidth of :
Ref: “Communication Systems” by S. Haykin and M. Moher, 5th ed
At receiver, how can and be found from

## Slide 15: Quadrature-Carrier Multiplexing (contd.)
Recall: under QAM, modulated signal given by:
and found from as shown in fig.
Thus, two independent message signals of bandwidth each sent using a bandwidth of
Ref: “Communication Systems” by S. Haykin and M. Moher, 5th ed
Twice as bandwidth-efficient as AM or DSB-SC

## Slide 16: Quadrature-Carrier Multiplexing (contd.)
Recall: under QAM, modulated signal given by:
Above, we have assumed that carrier signals used for modulation and demodulation are exactly synchronized
Suppose carrier signal used for:
  modulation is
  demodulation is , where is error
Upper demodulator output:
Ref: “Communication Systems” by S. Haykin and M. Moher, 5th ed
Called co-channel interference
Exercise: Find lower demodulator output and show that co-channel interference occurs for it as well

## Slide 17: Bandwidth Conservation
Quadrature-carrier multiplexing (QAM) scheme:
  transmits two independent signals of bandwidth each, using bandwidth of only
More bandwidth-efficient than AM and DSB-SC:
  which transmit only one signal of bandwidth using bandwidth
AM and DSB-SC bandwidth-inefficient since:
  upper and lower sidebands of message signal contain same information
  redundant to send both sidebands
Next, we study Single-Sideband (SSB) Modulation:
  similar to DSB-SC, except that only one sideband (either upper or lower) is transmitted
  transmits one signal of bandwidth using bandwidth
Ref: “Communication Systems” by S. Haykin and M. Moher, 5th ed

## Slide 18: Single-Sideband (SSB) Modulation
Conceptually, SSB modulated signal can be generated from a message signal as follows:
  first, modulate using a DSB-SC modulator
  then to the result, apply an ideal band-pass filter with passband:
    or
How can SSB modulated signal be demodulated at receiver?
  by multiplying it by and low-pass filtering the result
Practical difficulty in generation of SSB modulated signal:
  Band-pass filter with sharp transition from pass-band to stop-band required
Ref: B.P. Lathi, Z. Ding, “Modern Digital and Analog Communication Systems”, 4th ed.

## Slide 19: Single-Sideband (SSB) Modulation (contd.)
A common example of a message signal in which easy to generate SSB-modulated signal:
  speech signal
Speech signal has negligible amount of energy at low frequencies Hz)
  energy gap in spectrum near origin as shown in fig.
In this case, band-pass filter with sharp transition not required
Max. width of filter’s transition band, which separates pass-band from stop-band:
  twice the lowest frequency component of message signal, i.e.,
Ref: “Communication Systems” by S. Haykin and M. Moher, 5th ed

## Slide 20: Time Domain Representation of SSB Modulated Signal
To obtain time domain representation of an SSB modulated signal:
  we introduce Hilbert transform
Hilbert transform of signal defined to be:
Want to find Fourier transform, say , of
Exercise: Fourier transform of is
:
can be obtained from by passing it through LTI system with what amplitude and phase response?
  those shown in fig
How can we express SSB modulated version of in time domain using ?
Ref: B.P. Lathi, Z. Ding, “Modern Digital and Analog Communication Systems”, 4th ed.

## Slide 21: Time Domain Representation of SSB Modulated Signal (contd.)
We first obtain time-domain representation of:
  right sideband and
  left sideband
Then we use:
in terms of and :
Exercise:
Ref: B.P. Lathi, Z. Ding, “Modern Digital and Analog Communication Systems”, 4th ed.

## Slide 22: Demodulation of SSB Modulated Signal
Recall:
  Above representations confirm that SSB signal can be demodulated by:
    multiplying it by and low-pass filtering the result

## Slide 23: Vestigial-Sideband (VSB) Modulation
Recall: conceptually, SSB modulated signal can be generated from a message signal as follows:
  first, modulate using a DSB-SC modulator
  then to the result, apply an ideal band-pass filter with passband:
    or
Difficult to generate SSB modulated signal in case of baseband signals that do not have energy gap at origin
  for such signals, VSB modulation typically used instead of SSB modulation
VSB modulated signals easier to generate than SSB modulated signals
Also, bandwidth of VSB modulated signals typically only to higher than that of SSB modulated signals
Ref: B.P. Lathi, Z. Ding, “Modern Digital and Analog Communication Systems”, 4th ed.

## Slide 24: VSB Modulation (contd.)
Under VSB modulation:
  all of one sideband is transmitted (with some distortion)
  a small amount (vestige) of other sideband transmitted as well
Fig. shows VSB modulated signal
Ref: B.P. Lathi, Z. Ding, “Modern Digital and Analog Communication Systems”, 4th ed.

## Slide 25: VSB Modulation (contd.)
Fig. shows generation of VSB signal and its demodulation
Band-pass filter with frequency response has non-zero transition band
:
At demodulator, :
:
Ref: “Communication Systems” by S. Haykin and M. Moher, 5th ed
Substituting from 1), :
:
Sufficient condition for to be distortion-less version of :
  , for

## Slide 26: VSB Modulation (contd.)
Recall: sufficient condition for VSB-modulated signal to be distortion-less version of :
  , for
In practice, easy to design a band-pass filter that satisfies the condition in 1)
Amplitude response of such a filter for positive frequencies shown in fig.
Ref: “Communication Systems” by S. Haykin and M. Moher, 5th ed

## Slide 27: Exercise
Verify that we can also use the schemes shown in fig. for generating and demodulating a VSB signal provided following condition satisfied:
  , for
Thus, the condition:
  for
not necessary if filter at receiver designed appropriately
Ref: B.P. Lathi, Z. Ding, “Modern Digital and Analog Communication Systems”, 4th ed.