## Slide 1: Generation and Demodulation of Frequency Modulated Signals
Gaurav S. Kasbekar
Dept. of Electrical Engineering
IIT Bombay

## Slide 2: Introduction
Consider a carrier wave:
  ,
  where is “carrier amplitude” and
  is “carrier frequency”
Let be message signal, which is a baseband signal
Frequency modulated (FM) wave given by:
  where called “frequency sensitivity”
We will study circuits for generating FM signals and demodulating them

## Slide 3: Narrow-band FM (NBFM) Generation
Recall: FM signal given by:
Let
Recall: when for all , the signal called narrow-band FM signal
NBFM signal can be approximated by:
Signal in 2) can be generated using:
  a DSB-SC modulator as shown in fig.
Ref: B.P. Lathi, Z. Ding, “Modern Digital and Analog Communication Systems”, 4th ed.

## Slide 4: Distortion in NBFM Signal
Recall: NBFM signal can be approximated by:
Due to above approximation, there is some distortion in NBFM signal generated using above scheme
In terms of envelope and phase, relation in 1) can be rewritten as:
  where:
Ideally, envelope should be a constant
  since it is not constant, “amplitude distortion” is said to occur
Ideally, phase should be
  since , “frequency distortion” said to occur
However, note that since , above distortions are small

## Slide 5: Frequency Translation
We will discuss generation of a wide-band FM (WBFM) signal
One of the components needed for this is a “frequency translator”
  also known as “frequency converter” or “frequency mixer”
Suppose we have a modulated signal , whose spectrum is centred on carrier frequency :
Using , we want to generate a modulated signal , whose spectrum is centred on carrier frequency :
How can we generate from ?
  by multiplying with and band-pass filtering the product
  where if and if

## Slide 6: Frequency Multiplication
Frequency multiplier is another of the components used in generation of WBFM signal
Consider signal of form:
Frequency multiplier can be used to generate, from , signal of form:
  ,
  where is a positive integer and is a constant
How can we generate signal in 2) with from that in 1)?
  generate from and band-pass filter it
Generalization: how can we generate signal in 2) with arbitrary from that in 1)?
  generate from and band-pass filter it

## Slide 7: Indirect Method of Armstrong
Recall: FM signal given by:
Let
Recall: when for all , the signal called NBFM signal; otherwise called WBFM signal
In indirect method of Armstrong:
  first NBFM signal is generated (possibly using DSB-SC modulator method we discussed)
  then NBFM signal converted to WBFM signal
How can NBFM signal be converted to WBFM signal of desired center frequency and frequency deviation?
  by using frequency multipliers and frequency converters

## Slide 8: Example
Want to generate WBFM signal with:
  carrier frequency MHz and
  frequency deviation kHz
We initially generate NBFM signal with Hz and then convert it to required WBFM signal as shown in fig.
Note that we need to multiply Hz by 3072 to get kHz
However, if carrier frequency of kHz multiplied by 3072, then we get MHz
Hence, we need a frequency converter stage
Ref: B.P. Lathi, Z. Ding, “Modern Digital and Analog Communication Systems”, 4th ed.

## Slide 9: Example
Want to design an Armstrong indirect FM modulator to generate FM signal with:
  carrier frequency MHz and kHz
An NBFM generator is available with:
  kHz and Hz
Only frequency doublers can be used as multipliers
Also, a local oscillator (LO) with adjustable frequency between and kHz is available for frequency mixing
Solution:
  NBFM output is input to frequency multiplier with factor
  Frequency multiplier output is input to mixer with frequency kHz followed by band-pass filter that retains band around kHz
  Band-pass filter output is input to frequency multiplier with factor

## Slide 10: Direct Generation of Wideband FM Signals
In a voltage-controlled oscillator (VCO), frequency of output sinusoid controlled by input voltage
FM signal can be generated using a VCO with input being:
  message signal
Instantaneous frequency:
VCO can be implemented:
  using an operational amplifier and comparator
VCO can also be implemented:
  by varying the capacitance value according to in an oscillator containing inductor and capacitor
  e.g., Hartley oscillator, Colpitts oscillator
Implementation of capacitor with variable capacitance:
  reverse-biased diode acts as capacitor whose capacitance varies with bias voltage
  variable capacitor also known as “varicap”, “varactor” or “voltacap”

## Slide 11: Direct Generation of Wideband FM Signals (contd.)
In Hartley or Colpitts oscillator, frequency of oscillation given by:
Suppose capacitance varied using :
Then
  when
So ,
  where
Max. capacitance deviation:
  , where
  ,
  where (frequency deviation)
In practice, is small even in WBFM; hence distortion due to above approximation is small
So direct FM generation can be used to produce sufficient frequency deviation and does not require much frequency multiplication

## Slide 12: Demodulation of FM Signals

## Slide 13: Demodulation Using Differentiator
Recall: FM signal given by:
If a differentiator circuit is available, how can we demodulate FM signal?
  by inputting to differentiator and inputting its output to envelope detector
Output of differentiator:
Since , envelope detector can be used to recover from output of differentiator

## Slide 14: Demodulation Using Slope Circuit
Demodulation can be performed using “frequency discriminator”:
  consists of “slope circuit” followed by envelope detector
Suppose we want to demodulate FM signal of carrier frequency and transmission bandwidth
Ideal slope circuit has following transfer function:
  where is a constant
Want to find output, say , of slope circuit when input is FM signal:
Convenient to use:
  complex envelopes
Complex transfer function of :
Complex envelope of FM signal :
Ref: “Communication Systems” by S. Haykin and M. Moher, 5th ed

## Slide 15: Demodulation Using Slope Circuit (contd.)
Recall:
  Complex transfer function of :
  Complex envelope of FM signal :
Fourier transform of complex envelope of output of slope circuit:
Complex envelope of output of slope circuit:
By 1) and 2):
Output of slope circuit:
How can we obtain the message signal from ?
  using an envelope detector, since for all
Output of envelope detector:

## Slide 16: Demodulation Using Slope Circuit (contd.)
Recall: output of envelope detector:
DC bias term can be removed by:
    inputting output of envelope detector to a high-pass filter

## Slide 17: FM Stereo Multiplexing
In stereo audio, audio signal split into two signals, and :
  sent to left headphone and right headphone respectively
E.g.: and may correspond to a vocalist and an accompanist
FM stereo multiplexing enables transmission of the two signals and using the same FM carrier
FM stereo multiplexing must satisfy following requirements:
  The transmission must operate within allocated FM channel
  Has to be compatible with monophonic radio receivers
Frequency deviation of FM signal must be set taking requirement 1) into account

## Slide 18: FM Stereo Multiplexing (contd.)
Let be a kHz subcarrier
  Note: this subcarrier different from the carrier used for FM modulation
FM stereo transmitter shown in Fig.
Generated signal:
Ref: “Communication Systems” by S. Haykin and M. Moher, 5th ed
The signal then frequency modulates the main carrier to produce transmitted signal
The term included to:
  provide a reference for coherent detection of difference signal at receiver
  called “pilot signal”

## Slide 19: FM Stereo Multiplexing (contd.)
Recall: modulating signal:
At receiver, found using FM demodulation
How does a monophonic receiver process ?
  uses a low-pass filter to extract from and plays it out
How does a stereo receiver process ?
  as shown in Fig.
Ref: “Communication Systems” by S. Haykin and M. Moher, 5th ed

## Slide 20: Zero-Crossing Detectors
Want to demodulate FM signal:
First, FM signal is input to a hard limiter, i.e., circuit with following input-output characteristic:
Output of hard limiter is:
  square wave with time-varying pulse widths
How should square wave be processed to achieve FM demodulation?
Square wave is input to a digital counter:
  rate at which counter increments is directly proportional to instantaneous frequency of

## Slide 21: Phase-Locked Loop (PLL)
System that can be used for FM demodulation
Consists of following components connected together in form of feedback loop (see fig.):
  Multiplier
  Loop filter
  Voltage-Controlled Oscillator (VCO)
Input to PLL is FM signal:
Initially, VCO adjusted such that when control voltage is :
  Frequency of VCO is exactly carrier freq. of unmodulated carrier wave
  VCO output has a phase-shift w.r.t. unmodulated carrier wave
VCO output:
  where is frequency sensitivity of VCO
Objective: To recover message signal at VCO output, i.e., to ensure that:
  , where is a constant
Ref: “Communication Systems” by S. Haykin and M. Moher, 5th ed

## Slide 22: Non-Linear Model of PLL
Recall:
  where and
Multiplier output is low-pass filtered and is output of LPF
So :
  where and gain of multiplier is assumed to be
If loop filter is a linear system with impulse response , then :
So we get the following integro-differential equation:
  where
Equation in 1) difficult to analyse due to non-linear term
So next, we linearize the model to simplify the analysis
Ref: “Communication Systems” by S. Haykin and M. Moher, 5th ed

## Slide 23: Linear Model of PLL
Recall:
When , the PLL said to be in phase-lock
When for all , PLL said to be in near phase-lock
  then we use the approx.
Equation 1) reduces to:
How can we analyze 2)?
  take Fourier transforms on both sides
Ref: “Communication Systems” by S. Haykin and M. Moher, 5th ed

## Slide 24: Linear Model of PLL (contd.)
Recall:
Taking Fourier transforms, we get:
  ,
  where
Recall:
:
How should be chosen in order to ensure that is approx. proportional to ?
  We choose such that in the baseband
:
So :
Thus, frequency demodulation achieved
Ref: “Communication Systems” by S. Haykin and M. Moher, 5th ed

## Slide 25: Effect of Sending FM Signal over Non-linear Channel
Consider FM signal:
  where
Sent over a channel with following input-output characteristic:
  where , and are constants
Recall the trigonometric identity:
Output of channel:
Can message signal be recovered from ?
  Yes, assuming that is much larger than bandwidth of FM signal
Recovery:
  Input to band-pass filter with mid-band frequency
Output:
is scaled version of
Thus, FM signals robust to transmission over non-linear channels of above type
So FM widely used in satellite communication systems
  permits the use of highly non-linear amplifiers, which are required for producing a high-power output at radio frequencies

## Slide 26: Effect of Sending AM Signal over Non-linear Channel
Consider AM signal:
Sent over a channel with following input-output characteristic:
  where , and are constants
Output of channel:
Can message signal be recovered from ?
  Difficult to recover it; cannot be recovered using envelope detection
Thus, AM signal gets distorted when transmitted over non-linear channels of above type

## Slide 27: Amplitude Variations in FM Signal
Recall: FM signal:
  When FM signal sent over a channel, several factors (e.g., channel noise and fading) can cause amplitude to vary
  So received signal is of form:
  If directly input to FM demodulator:
    output would be distorted version of
  E.g.:
    Recall that FM signal can be demodulated by inputting it to differentiator and inputting output of differentiator to an envelope detector
    Output of this differentiator when :
    When is not a constant:
      There is an additional term containing in output of differentiator
      Even if this term is neglected, output of envelope detector is ; hence, output is distorted version of
  Hence, technique required to suppress variation in amplitude of received signal before inputting it to FM demodulator

## Slide 28: Amplitude Variations in FM Signal (contd.)
  Recall: received signal is of form
  Technique to suppress variation in amplitude of received signal :
    Input to a hard limiter and input the output of hard limiter to a band-pass filter centred at
  Intuitive justification for fact that above technique indeed suppresses amplitude variations, while keeping phase unchanged:
    since is roughly constant, output of hard limiter is of the form:
    Output of band-pass filter is